## Slide 1
TRACE Launcher
Prepro
Perturb the TRACE parameters listed in the list of parameters file according to the values specified in design matrix
Generate directory structures that contains spawned trace input decks
Execute
Submit and manage TRACE jobs in parallel (in sequential batches)
Convert XTV to DMX to save drive space
Do directory cleanup to further reduce the space requirements
Post-process
Postprocess each xtv files and extract the variables listed in the list of graphic variables file into separate csv files.
List of Graphic Variables
CSV
Ready to be post- processed further for sensitivity or uncertainty analyses
Base TRACE
List of Parameters
Design Matrix
TRACE Executable
Aptplot Executable
Inputs & Aux files
Driver Scripts
Outputs
prepro info file
exec info file
postpro info file
Notes: Generic flowchart of trace-simexp

## Slide 2
TRACE Launcher
Sample Module
Simple Random Sampling (SRS)
Latin Hypercube Sampling (LHS)
L2-discrepancy optimized (space-filling) Latin Hypercube Sampling (optLHS)
Sobol’ sequence launcher (sobol)
Validation points generator
CSV
Sensitivity Analysis
Generate Samples
Driver Script Executables
Computer Codes + Post-processing (feature extraction)
Externally Implemented
CSV
Model Outputs
Sensitivity Analysis Post-processor Modules
1st Order Sobol Indices (sobol)
Total Order Sobol Indices (sobol)
Morris Screening Method (morris)
Linear Model-Based Method Pearson Correlation Coeff. (CC), Standardized Regression Coef. (SRCC), Partial CC
Rank-transformed methods Spearman CC, SR(ank)RC, PR(ank)CC
Etc.
CSV
Design Matrix (previously generated)
Design Matrix
Model Execution
CSV
Sensitivity Measures
Future Development
Implemented
Notes: Generic flowchart of trace-simexp